## KRIEGER SPECIALTY PRODUCTS

### 4880 Gregg Road

#### Pico Rivera, CA  90660

Tel:  562-695-0645

Fax:  562-692-0146

SECTION 08 34 74

SOUND CONTROL WOOD DOOR ASSEMBLIES

NOTE ** Krieger Specialty Products also manufactures bullet-resistant, blast-resistant, radio frequency shielding, thermal shielding and stainless steel doors, frames and windows.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	This section includes wood acoustical door and frame assemblies where shown on the plans, as specified herein, and as needed for complete and proper Installation.

1.2	RELATED SECTIONS

NOTE ** Delete any sections below not relevant to this project; add others as required.

A.	Section 08 70 00 - Door Hardware.

B.	Section 08 80 00 - Glazing.

C.	Section 09 90 00 - Paints and Coatings.

1.4	REFERENCES

NOTE ** Delete references from the list below that are not actually required by the text of the edited section.

A.	ANSI/WDMA I.S.1-A. - Wood Flush Doors.

B.	ASTM A 1008 - Standard Specification for Steel, Carbon, Cold-Rolled Sheet, Commercial Quality.

C.	ASTM A 569 - Standard Specification for Steel, Carbon, (0.15 Maximum Percent), Hot-Rolled Sheet and Strip, Commercial Quality.

D.	ASTM A 653/A 653M - Standard Specification for Steel Sheet, Zinc Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot Dip Process.

E.	ASTM E 90 - Standard Test Method for Laboratory Measurement of Airborne-Sound Transmission Loss of Building Partitions.

F.	ASTM E 336 - Standard Test Method for Measurement of Airborne Sound Insulation in Buildings.

G.	ASTM E 413 - Classification for Determination of Sound Transmission Class.

H.	HMMA 840 - Installation and Storage of Hollow Metal Doors and Frames; Hollow Metal Manufacturers Association.

I.	ISO 4586-2 - High Pressure Decorative Laminates; International Standards Organization.

J.	NEMA LD 3-1995 - High Pressure Decorative Laminates; National Electrical Manufacturers Association.

1.5	SYSTEM DESCRIPTION

A.	Design requirements:  Acoustical door assemblies to include doors, frames, and door hardware to include gasketing systems, retainers and retainer covers, automatic or fixed door bottoms, cam-lift hinges, thresholds, and sills, required to achieve specified performance requirements.

NOTE**Insert Sound Transmission Class (STC) requirements (value 33-55) in the following paragraph.

B.	Performance requirements:  Sound Transmission Coefficient rating of STC ____ for installed assembly, when tested as operable door assembly in accordance with ASTM E 90 and ASTM E 413.

1.6	SUBMITTALS

A.	Submit under provisions of Section 01300.

NOTE**Delete one of the following two paragraphs; first is for wood doors, second is for steel doors.

B.	Product data:  Indicate door materials and construction; indicate veneer species_______________________ type and characteristics.

C.	Product data:  Indicate door materials and construction.

D.	Shop drawings:  Indicate door opening criteria, elevations, sizes, types, swings; identify and detail cutouts.

E.	Selection samples:  Two (2) sets samples of available door finishes, representing manufacturer's full range.

F.	Verification samples:  Two (2) samples of door construction, 12 inches square in size, cut from corner of door.

G.	Quality assurance submittals:

1.	Test Reports:

a.	Certified laboratory reports, performed in accordance with ASTM E90 and ASTM E 413, from independent testing laboratory qualified under the National Voluntary Laboratory Accreditation Program (NVLAP) supporting compliance of assemblies to specified requirements.

b.	Minimum five (5) field tests, performed in accordance with ASTM E 336 and ASTM E 413 by five separate independent testing agencies, substantiating acoustical performance when installed at no less than four (4) FSTC ratings below the specified STC rating.

2.	Certificates:

a.	Contractor's certification that:

1)	Products of this section, as provided, meet or exceed specified requirements.

2)	Manufacturer of products of this section meet specified qualifications.

3.	Manufacturer's instructions:  Printed installation instructions for each component.

H.	Closeout submittals:

1.	Warranty documents, executed by manufacturer in Owner's name.

2.	Operation and maintenance data for assembly components.

3.	Certified statement of manufacturer's authorized representative, as specified in FIELD QUALITY CONTROL Article of PART 3 of this section.

4.	Certified test reports of independent testing agency, as specified in FIELD QUALITY CONTROL Article of PART 3 of this section.

1.7	QUALITY ASSURANCE

A.	Qualifications:

1.	Manufacturer:  Minimum five (5) years documented experience producing systems specified in this section.

2.	Installer:  Minimum five (5) years documented experience producing systems specified in this section, and approved by manufacturer.

1.8	DELIVERY, STORAGE, AND HANDLING

A.	Store frames in accordance with requirements of HMMA 840.

B.	Store doors in accordance with requirements of HMMA 840.

C.	Remove wraps or covers from doors and frames upon delivery at the building site; clean and touch-up scratches or disfigurement caused by shipping or handling promptly with rust inhibitive primer.

D.	Store units on planks or dunnage in a dry location; store doors in a vertical position spaced by blocking.

E.	Store units covered to protect them from damage, but permitting air circulation.

1.9	SCHEDULING

A.	Furnish manufacturer's mounting templates for door hardware specified in Section 08710 to manufacturer of products of this section in time for factory preparation for door hardware.

PART 2	PRODUCTS

2.1	MANUFACTURERS

A.	Acceptable manufacturer:  Krieger Steel Products, 4880 Gregg Road, Pico Rivera CA 90660; Telephone 562-695-0645, FAX 562-692-0146.

B.  	Substitutions:  Not permitted.

C.	Unless otherwise specified for an individual product or material, supply all products specified in this section from the same manufacturer.

2.2	DOOR SYSTEMS

A.	Provide acoustical assemblies complete with door, frame, anchors, sound seals, hinges, and cutouts and reinforcements for hardware items listed or required.

B.	Where indicated on the plans or otherwise required, provide factory-installed glazed vision light assembly in dimensions meeting specified STC rating.

C.	Acoustical material:  Manufacturer's standard for required STC rating.

D.	Primer:  Meeting ASTM B 117 salt spray for 150 hours, and ASTM D 1735 water fog test for organic coatings for 200 hours.

E.	Glazing:  Specified in Section 08 80 00.

2.3	DOORS

A.	Materials:

Doors shall be 2” thick, constructed of wood veneer of species indicated with a sound-deadening core.

- Construction:

  - All doors shall be of the types and sizes shown on approved shop drawings and shall have a 1-3/4 thick acoustical core.  Doors shall be clad with 3-ply crossband veneer for 7-ply door construction.  All adhesives, as well as warp tolerances, shall be in accordance with ANSI / NWWD 1.S.1-A

  - Face veneers, stile and rail edges, and appearance features match the doors approved under Section 08 14 00.

3.	Factory finish sound control doors to match the control sample approved by the Contracting Officer.  Finish is required on all exposed surfaces of door including top and bottom edges.

- Hardware reinforcements:  Doors shall be mortised and reinforced for fully

templated hardware, only in accordance with the approved hardware schedule and templates provided by the hardware contractor.  Surface applied hardware are drilled on site by others.

NOTE**Delete the following two paragraphs if vision lites not required.

D.	Vision lites:

1.	Factory-assemble lites in doors indicated to have lites, using glazing materials and assembly methods indicated on approved shop drawings for required STC rating; field assembly not permitted.

2.	Fabricate dual-glazed lites permitting individual removal of each glazing pane.

E.	Loose stops:

1.	Fabricate of minimum 12 gage steel, with factory-drilled and countersunk holes for fasteners.

2.	Form stops for mitered corner joints.

3.	Supply cadmium-coated or zinc-coated fasteners, size and quantity required for fastener holes.

F.  Door hardware:

4.   Supply compression ( magnetic seals are not acceptable) acoustical gasketing systems, retainers, retainer covers, automatic door bottoms or fixed door bottoms, cam-lift hinges ( where applicable to the STC rating), thresholds, and sills as indicated on Architect-approved shop drawings, or specified in manufacturer's product data for project conditions, to achieve specified performance requirements.

5.   All other door hardware is specified in Section 08710.

NOTE ** Delete the following paragraph if no acoustical panels required.

2.4	PANELS

Sound control panels shall be made of the same materials and construction and finished in same way as specified in Section 2.3 of this specification.

2.5    FRAMES

A.	Materials:

6.	Frames shall be constructed of 14 gage minimum thickness commercial quality, level, cold rolled steel conforming to ASTM 1008 and free of scale, pitting or other surface defects.

7.	Exterior frames shall have a zinc coating by the hot dip process conforming to ASTM A526 (G90) with a coating not less than 1.25 ounces per square foot both sides.

- Construction:

1. Frames shall be welded units with integral trim, of the sizes and shapes shown on Approved Shop Drawings.  Knocked-down frames will not be accepted.  If field splices are required because of shipping limitations, such splices should be field welded after installation.

2 .Corner joints shall have all contact edges closed tight, with trim faces mitered        and continuously welded.  The use of gussets will not be permitted.

C.	Hardware reinforcements:

- Frames shall be mortised, reinforced, drilled and tapped frames for all templated hardware, only in accordance with final approved hardware schedule and templates provided by the hardware supplier.  Where surface mounted hardware and non-templated mortised hardware is to be applied, frames shall be reinforced, with all drilling and tapping done in the field by others.

D.  Jamb Anchors

D.	Jamb anchors:

1.	Wall Anchors to be fabricated of same material as frame material; weld anchors inside each jamb for wall anchorage.

2.	Provide anchor types for indicated adjacent wall construction:

a)	Frames for installation in masonry walls:  Adjustable jamb anchors, 16 gage, T-shape type.

b)	Frames for installation in stud partitions shall be provided with 16 gage steel zee anchors not more than 24” O. C. welded inside each jamb.

E.  Floor Anchors

1.  Fabricate of same material as frame material: 16 gage.

a)	Weld anchors inside each jamb for floor anchorage.

F.	Plaster guards:  Fabricate from minimum 22 gage steel; weld in place at hardware mortises on frames to be set in plaster, masonry, or concrete openings.

G.  	Provide welded frames with temporary steel spreader welded to jamb feet for bracing during shipping and handling.  The steel spreader is not to be used for installation purposes.

H.	All tool marks and surface imperfections shall be removed and exposed faces of all welded joints shall be dressed smooth.  Assemblies shall be treated and shall be coated on all accessible surfaces with rust-inhibitive primer which meets ASTM B117 salt spray for 150 hours, and ASTM D1735 water fog test for organic coatings for 200 hours, and which is fully cured prior to shipment.

  - SILL CONDITION

Where indicated on the drawings, furnish a smooth aluminum threshold ( lipped thresholds are not acceptable) for the door bottom to seal against, when the door is in the closed position.  The minimum width of the threshold shall be door thickness plus 4” to allow the threshold to extend a minimum of 1 ” beyond the face of the door on both sides of the door.  For openings where carpet extends on each side of the opening, the threshold height shall be 1/8” greater in height than the carpet thickness.

NOTE ** Finished floor is defined as the top surface of the floor, except when resilient tile or carpet is used, when it is the top of the concrete slab.

PART 3	EXECUTION

3.1	INSTALLATION

Note to Architect:  Proper installation is essential to the proper performance of acoustical door and frame assemblies.

It shall be the responsibility of the general contractor to perform the following:

A.	Verification of conditions:

1.	Prior to installation, check and correct frames for size, swing, squareness, alignment, twist and plumb.

2.	Verify openings are in accordance with approved shop drawings.

B.      Installer's examination:

3.	Have installer of this section examine conditions under which construction activities of this section are to be performed, then submit written notification if such conditions are unacceptable.

4.	Transmit two copies of installer's report to Architect within 24 hours of receipt.

5.	Beginning construction activities of this section before unacceptable conditions have been corrected is prohibited.

6.	Beginning construction activities of this section indicates installer's acceptance of conditions.

C.	Solidly grout fill frames where so indicated on the drawings or the approved submittals, eliminating all voids.  The flanking path normally found behind the frame must be packed with either 6-12 lb rock wool insulation or grout filled to assure minimum sound transmission.

3.2	PREPARATION

A.	Remove steel spreaders from welded frames prior to installation; use of spreaders for installation purposes not permitted.

3.3	INSTALLATION

A.	Install units in accordance with approved shop drawings and manufacturer's printed installation instructions; in addition, install steel components in accordance with HMMA 840.

B.	Fill voids between concealed side of frame and adjacent wall construction with dense fiberglass or lightweight gypsum plaster in accordance with approved shop drawings or manufacturer's printed installation instructions.

C.	Finish surfaces having abrasion damage smooth; touch-up with rust inhibitive primer.

D.	Install gasketing systems, retainers, retainer covers, automatic door bottoms, fixed door bottoms, cam-lift hinges, thresholds, and sills in accordance with manufacturer's printed instructions.

NOTE ** Verify section references in the following two paragraphs.

E.	Installation of all other door hardware is specified in Section 08 71 00.

F.	Field painting is specified in Section 09 90 00.

G.	Site tolerances:  Do not exceed the following installation tolerances:

1.	Squareness:  Plus or minus 1/16 inch measured on a line, 90 degrees from one jamb, at the upper corner of the frame at the other jamb.

2.	Alignment:  Plus or minus 1/16 inch measured on jambs on a horizontal line parallel to the plane of the wall.

3.	Twist:  Plus or minus 1/16 inch measured at face corners of jambs on parallel lines perpendicular to the plane of the wall.

4.	Plumb:  Plus or minus 1/16 inch measured on the jamb at the floor.

NOTE ** The above tolerances provide a reasonable guideline for proper installation of hollow metal frames. However, it should be noted that the cumulative effect of the tolerances at their maximum levels will result in sufficient misalignment to prevent the door from functioning properly. Care should be taken to keep each of these tolerances as close to zero as possible.

3.4	FIELD QUALITY CONTROL

A.	Engage and pay for the field services of manufacturer's authorized representative to:

1.	Inspect completed installation of door and frame assemblies.

2.	Test all components through a minimum of ten complete cycles of operation.

3.	Verify each component is correctly installed.

4.	Direct installer in adjusting components for correct operation.

5.	Issue certified statement of compliance of installed door and frame assemblies to Architect-approved shop drawings.

6.	Instruct Owner's maintenance personnel in correct operation and maintenance procedures for components of door and frame assemblies.

B.	Engage and pay for the services of independent testing agency to:

1.	Test door and frame assemblies selected by Owner or Architect in accordance with ASTM E 336.

2.	Issue certified report documenting compliance of installed door and frame assemblies to specified acoustical performance requirements.

C.	Notify Architect a minimum of seven (7) calendar days prior to scheduled testing dates.

  - MAINTENANCE

Instruct the Owner’s Maintenance Personnel regarding the proper operation and maintenance of these doors.

END OF SECTION